Model:			ELSA

Type:				Open circuit, constant flow compressed air escape 				breathing apparatus

Design Specification:	EN1146

General Description

Open circuit, compressed air, constant flow escape breathing apparatus generally comprising: cylinder with combined cylinder valve and reducer, supply hose to constant flow hood and stowage bag.

The apparatus is available in both 10 and 15 minute versions with the bag in either  high visibility PVC or black anti-static polyurethane materials.

Additional Features:

The ELSA is a escape breathing apparatus which provides a constant flow of air into the hood at 38 lpm providing a duration in excess of 10 or 15 minutes.

The combined cylinder valve and pressure reducer is activated upon opening the bag whereby a pin which is attached to the flap of the bag via a strap.

The 10 minute apparatus utilises a 2 litre, 200 bar alloy steel cylinder, whereas the 15 minute apparatus uses a 3 litre, 200 bar alloy steel cylinder. Cylinders are manufactured to EC specifications. Other specifications are available on request.

The combined cylinder valve and pressure reducer is fitted to the cylinder. It features a spring and piston mechanism with a fixed orifice outlet. The valve incorporates a warning whistle that sounds when the designated duration is reached. A pressure relief valve, which operates at approximately 11.5 bar, protects the system from over pressurisation.

The charging connector features a EN 144-2 (5/8” BSP female) thread.

The hoods are available in two versions, the standard type and a double sided “easy clean” version.  The hoods are fabricated in high visibility flame resistant PVC or PVC coated materials with an elastomeric neck seal. The inner mask prevents visor misting and minimises carbon dioxide dead space.

The standard bag is fabricated from high visibility orange materials. The anti-static bag is fabricated from black polyurethane.

The opening flap is held closed by Velcro strips and an adjustable webbing neck strap supports the bag when in use. This strap can be attached in different places to hold the apparatus in two different orientations. A transparent window is provided to allow the cylinder contents gauge and activating pin to be checked without opening the bag. A tamperproof tag is supplied to prevent unauthorised entry into the bag.

An optional waistbelt can be worn with all versions of the bag.

Weights:

10 minute versions (charged)		4.2kg

15 minute versions (charged)		6.15kg

Dimensions 520mm x 340mm x 135mm